DECREE OF THE DIRECTOR GENERAL OF POST AND TELECOMMUNICATION

NUMBER : 210/DIRJEN/2009

ON

AMENDMENT TO THE DECREE OF THE DIRECRTOR GENERAL OF POST AND TELECOMMUNICATION NUMBER : 95/DIRJEN/2008 ON TECHNICAL REQUIREMENTS OF TELECOMMUNICATION TOOLS AND EQUIPMENT BASE STATION BROADBAND WIRELESS ACCESS (BWA) NOMADIC AT FREQUENCY BAND OF 2.3 GHz

BY THE GRACE OF GOD THE ALMIGHTY

DIRECTOR GENERAL OF POST AND TELECOMMUNICATION,

Considering:         a   that in line with the provision of the Decree  of  the Director

General   of   Post    and    Telecommunication       Number

95/DIRJEN/2008      on     Technical     Requirements     of

Telecommunication   Tools  and  Equipment   Base Station

Broadband Wireless Access (BWA) Nomadic at Frequency                                  	Band  of 2.3 GHz,   the   communication  system  works  at                                  	frequency of 2300-2390 MHz;

b. that    Article   2   of   the   Decree    of    the   Minister  of

Communication   and   Information Technology  Number

08/PER/M.KOMINFO/01/09   on   Assigning   the   Radio

Frequency Band For the Purpose of Wireless Broadband

Service at   frequency   band of 2.3 GHz, determines that

the   radio    frequency    band     of    2300-2400 MHz  is

assigned    for    the    purpose of    wireless   broadband

service with time division duplex mode (TDD);

c. that based on considerations mentioned in  points a and b,

it  is  considered  necessary  to  amend  the Decree of the

Director   General   of    Post    and     Telecommunication

Number 95/DIRJEN/2008  on  Technical Requirements of

Telecommunication      Tools    and    Equipment      Base

Station Broadband Wireless Access  (BWA)  Nomadic  at

Frequency Band of 2.3 GHz.

Bearing in mind:   1. Law of the Republic of Indonesia Number 36 Year 1999 on

Telecommunication   (State Gazette  of  the   Republic    of

Indonesia Number 154 Year 1999, Additional State Gazette

of the Republic of Indonesia Number 3881);

.

- Government Regulation of the Republic of Indonesia Number 52 Year 2000 on the Provision of Telecommunication (State Gazette of the Republic of Indonesia Number 107 Year 2000, Additional State Gazette of the Republic of Indonesia Number 3980);

- Government Regulation of the Republic of Indonesia Number 53 Year 2000 on Use of Radio Frequency Spectrum and Satellite Orbit (State Gazette of the Republic of Indonesia Number 108 Year 2000, Additional State Gazette of the Republic of Indonesia Number 3981);

- Decree of the President of the Republic of Indonesia Number 9 Year 2005 on Positions, Tasks, Functions, Organizational Structure and Working of State Ministries of the Republic of Indonesia as amended latest by the Decree of the President of the Republic of Indonesia Number 20 Year 2008;

- Decree of the President of the Republic of Indonesia Number 10 Year 2005 on Organizational Units and Functions of Echelon I of State Ministries of the Republic of Indonesia as amended latest by  the Decree of the President of the Republic of Indonesia Number 21 Year 2008;

- Decision of the Minister of Communication Number KM. 3  Year 2001 on Technical Requirements of Telecommunication Tools and Equipment;

- Decree of the Minister of Communication and Information Technology Number 03/P/M.Kominfo/5/2005  on Adjustment of Nomenclatures of a number of Decisions/Decrees of the Minister of Communication which regulate Special Material Contents in the field of Post and Telecommunication;

- Decree of the Minister of Communication and Information Technology Number 25/P/M.Kominfo/7/2008 on Organizational Structure and Working of the Department of Communication and Information Technology;

- Decree of the Minister of Communication and Information Technology Number 29/PER/M.KOMINFO/09/2008 on Certification of Telecommunication Tools and Equipment.

DECIDES

To ratify              : DECREE OF THE DIRECTOR GENERAL OF POST AND

TELECOMMUNICATION ON AMENDMENT TO THE   DECREE OF THE DIRECTOR GENERAL OF POST AND TELECOMMUNICATION NUMBER 95/DIRJEN/2008 ON TECHNICAL REQUIREMENTS OF TELECOMMUNICATION TOOLS AND EQUIPMENT BASE STATION BROADBAND WIRELESS ACCESS (BWA) NOMADIC AT FREQUENCY BAND OF 2.3 GHz

Article I

Some provisions in the Attachment of the Decree of the Director General of Post and Telecommunication Number 95/DIRJEN/2008 on Technical Requirements of Telecommunication Tools and Equipment Base Station  Broadband Wireless Access (BWA) Nomadic at Frequency Band of 2.3 GHz is amended as follows

- The provision of CHAPTER I on General Provisions, point 2 is amended to read as follows:

- Definition

What is meant by tools and equipment of BS BWA 23 System in this standard is a communication system that works at frequency of 2,300 – 2,400 MHz and has the affordability to conduct broadband wireless transmission, multi-service capability, differentiation of treatment in line with traffic priority, service quality standard and security mechanism.

- The provision of Point 2.4.1 canalization for canal width of 3.75 MHz is amended to read as follows:

    - Canalization for canal width of 3.75 MHz

2300

Figure 3. Canalization for canal width of 3.75 MHz

Table 2. Center frequency of canalization for canal width of 3.75 MHz

- The provision of Point 2.4.2 canalization for canal width of 7.5 MHZ is amended as follows:

    - Canalization for canal width of 7.5 MHz

2300                                                                                                                                                                              2400

Figure 4. Canalization for canal width of 7.5 MHz

Table 2.  Center frequency of canalization for canal width of 7.5 MHz

Article II

This Decree shall come into force on the date of its ratification.

Done at:                JAKARTA

On       :  September 9, 2009

_______________________

Acting DIRECTOR GENERAL OF POST AND TELECOMMUNICATION,

Signed

BASUKI YUSUF ISKANDAR

Copies of this Decree are sent to:

- Minister of Communication and Information Technology;

- Secretary of the Directorate General of Post and Telecommunication;

- Directors within the Directorate General of Post and Telecommunication;

- Head of the House for Telecommunication Equipment Testing.