DECISION OF THE MINISTER OF COMMUNICATION AND INFORMATION TECHNOLOGY

NUMBER : 181/KEP/M.KOMINFO/12/2006

ON

CANAL ALLOCATION OF RADIO FREQUENCY BAND OF 800 MHZ FOR THE PROVISION OF WIRELESS LOCAL FIXED NETWORK WITH LIMITED

MOBILITY AND THE PROVISION OF CELLULAR MOBILE NETWORK

BY THE GRACE OF GOD THE ALMIGHTY

MINISTER OF COMMUNICATION AND INFORMATION TECHNOLOGY

Considering:          a.  that the Decree of the Minister of Communication and

Information Technology Number: 01/PER/M.KOMINFO

/1/2006 on Structuring the Radio Frequency Band of 2.1

GHz for the Provision of IMT-2000 Cellular Mobile Network

has defined the provision that  the provider of wireless local

fixed network with limited mobility using radio frequency

band of 1.9 GHz may only use the concerned radio

frequency band up to 31 December 2007 and thereafter

has to move to radio frequency band of 800 MHz;

- that within the framework of improving efficiency on the use of radio frequency band and after having undergone an in-depth evaluation, it is deemed necessary to undertake structuring of the use of radio frequency band of 800 MHz which is presently being used by providers of wireless local fixed network with limited mobility and providers of cellular mobile network;

- that for the purpose mentioned in points a and b, it is considered necessary to define the provision on canal allocation of radio frequency band of 800 MHz for the provision of wireless local fixed network with limited mobiliy and the provision of cellular mobile network by ratifying a Decision of the Minister of Communication and Information Technology.

Bearing in mind: 1.  Law of the Republic of Indonesia Number 36 Year 1999

on Telecommunication (State Gazette of the Republic of

Indonesia Number 154 Year 1999, Additional State

Gazette of the Republic of Indonesia Number 3881);

.

- Government Regulation of the Republic of Indonesia Number 52 Year 2000 on Provision of Telecommunication (State Gazette of the Republic of Indonesia Number 107 Year 2000, Additional State Gazette of the Republic of Indonesia Number 3980);

- Government Regulation of the Republic of Indonesia Number 53 Year 2000 on Use of Radio Frequency Spectrum and Satellite Orbit (State Gazette of the Republic of Indonesia Number 108 Year 2000, Additional State Gazette of the Republic of Indonesia Number 3981);

- Government Regulation of the Republic of Indonesia Number 28 Year 2005 on Tariffs of the Kinds of Non-Tax State Income Applicable at the Department of Communication and Information Technology (State Gazette of the Republic of Indonesia Number 57 Year 2005, Additional State Gazette of the Republic of Indonesia Number 4511);

- Decree of the President of the Republic of Indonesia Number 9 Year 2005 on Positions, Tasks, Functions, Organizational Structure and Working of State Ministries of the Republic of Indonesia;

- Decree of the President of the Republic of Indonesia Number 10 Year 2005 on Organizational Units and Functions of Echelon I of State Ministries of the Republic of Indonesia as amended by the Decree of the President of the Republic of Indonesia Number 15 Year 2005;

- Decision of the Minister of Communication Number KM. 20  Year 2001 on Provision of Telecommunication Network as amended by the Decision of the Minister of Communication  Number KM. 29 Year 2004;

- Decision of the Minister of Communication Number: KM. 21 Year 2001 on Provision of Telecommunication Service  as amended by the Decision of the Minister of Communication Number KM. 30 Year 2004;

- Decision of the Minister of Communication Number KM. 31 Year 2003 on the Determination of the Indonesian Telecommunication Regulatory Body as amended by the Decree of the Minister of Communication and Information Technology Number 25/P/M.Kominfo/11/2005;

- Decision of the Minister of Communication Number: KM. 35 Year 2004 on Provision of Wireless Local Fixed Network with Limited Mobility;

- Decree of the Minister of Communication and Information Technology Number 01/P/M.Kominfo/1/2005 on Organizational Structure and Working of the Department of Communication and Information Technology;

- Decree of the Minister of Communication and Information Technology Number: 03/P./M.Kominfo/5/2005 on Adjustment of Nomenclatures of a number of Decisions/Decrees of the Minister of Communication which regulate Special Material Contents in the field of Post and Telecommunication;

- Decree of the Minister of Communication and Information Technology Number 17/PER/M.KOMINFO/10/2005 on Procedure of Licensing and Operational Provision on the Use of Radio Frequency Spectrum;

- Decree of the Minister of Communication and Information Technology Number 19/PER.KOMINFO/10/2005 on  Guideline for the Implementation of Tariffs of Non-Tax State Income emanating from the Charges for the Right to Use (CRU) Radio Frequency Spectrum;

- Decree of the Minister of Communication and Information Technology Number 01/PER.KOMINFO/1/2006 on Structuring the Radio Frequency Band of 2.1 GHz for the Provision of IMT-2000 Cellular Mobile Network;

- Decree of the Minister of Communication and Information Technology Number 08/Per/M.KOMINFO/02/2006 on Interconnection.

DECIDES

To ratify             :  DECISION OF THE MINISTER OF COMMUNICATION AND

INFORMATION TECHNOLOGY ON CANAL ALLOCATION

OF RADIO FREQUENCY BAND OF 800 MHZ FOR THE

PROVISION OF WIRELESS LOCAL FIXED NETWORK

WITH LIMITED MOBILITY AND THE PROVISION OF

CELLULAR MOBILE NETWORK

FIRST          :	Allocate radio frequency band of 800 MHz for the provision of wireless local fixed network with limited mobility and the provision of cellular mobile network as under :

Mode of FDD. 825 – 845 MHz in pair with 870 – 890 MHz.

SECOND     :	The use of radio frequency band as stated in the FIRST Dictum refers to the arrangement of 3GPP2 C.SOO57-B Band Class Specification for CDMA2000 Spread Spectrum Systems, Band Class 0 (800 MHz) Spreading Rate 1.

THIRD         :	Allocate radio frequency canal of radio frequency band of 800 MHz for providers of telecommunication network as under :

- PT. Bakrie Telecom, as provider of wireless local fixed network with limited mobility, is allocated with radio frequency canals numbered 37, 78, and 119.

- PT. Telekomunikasi Indonesia, as provider of wireless local fixed network with limited mobility, is allocated with radio frequency canals numbered 201, 242, and 283.

- PT. Komunikasi Selular Indonesia (Komselindo), PT. Metro Selular Nusantara (Metrosel) and PT. Telekomunikasi Seluler Raya (Telesera), as providers of cellular mobile network, each is allocated with radio frequency canal in the service area in accordance with the provision licenses owned by them with canal numbers of 384, 425, 466, and 507.

- PT. Indosat, as provider of wireless local fixed network with limited mobility, is allocated with radio frequency canals numbered 589 and 630.

FOURTH    :	The carrier of radio frequency (carrier frequency) for mobile station and base station for radio frequency canals as stated in the THIRD Dictum is as indicated in the Attachment of this Ministerial Decision.

FIFTH        :	The bandwidth that may be used for radio frequency canals as stated in the THIRD Dictum is 1.23 MHz.

SIXTH       :	Adjustment in the use of radio frequency canal as stated in the THIRD Dictum is carried out gradually and is finalized at the latest up to 31 December 2007.

SEVENTH    :	a.  Allocate radio frequency canal with canal number of 160 as

a reserve for PT. Bakrie Telecom or PT. Telekomunikasi

Indonesia, the use of which will be determined later based

on evaluation result by the Minister considering:

      - the optimization in making use of radio frequency canal;

      - the quantity of network development; and

      - the number of customers,

of the two telecommunication providers.

- Allocate radio frequency canal with canal number of 548 as a reserve for PT. Komunikasi Selular Indonesia (Komselindo), PT. Metro Selular Nusantara (Metrosel), PT. Telekomunikasi Seluler Raya (Telesera), or PT. Indosat, the use of which will be determined later based on evaluation result by the Minister considering :

  - the optimization in making use of radio frequency canal;

  - the quantity of network development; and

  - the number of customers,

of the four telecommunication providers.

- The evaluation as stated in the SEVENTH Dictum points a and b is conducted at the latest two (2) years as from the ratification of this Ministerial Decision.

EIGHTH       :	The providers of telecommunication network as stated in the THIRD Dictum shall pay Charges for the Right to Use (CRU) radio frequency in accordance with the provision of the prevailing regulation.

NINTH         :	The providers of telecommunication network as stated in the THIRD Dictum shall adjust :

      - the licenses of telecommunication network provision owned by them including but not limited to their network development plan; and

      - the licenses for the use of radio frequency spectrum owned by them,

at the latest three (3) months as from the ratification of this Ministerial Decision.

TENTH        :	Violation against the provision of this Ministerial Decision will be given sanctions in accordance with the provision of the prevailing regulation.

ELEVENTH :	This Ministerial Decision shall come into force on the date of its ratification.

Done at:                 JAKARTA

On        : December 12, 2006

_______________________

MINISTER OF COMMUNICATION AND INFORMATION TECHNOLOGY,

Signed

SOFYAN A. DJALIL

Copies of this Decision are sent to:

- Chairman of the Capital Investment Coordination Body;

- Director General of Post and Telecommunication;

- Members of Telecommunication Regulatory Committee of the Indonesian Telecommunication Regulatory Body.