//DECREE OF THE DIRECTOR GENERAL OF POST AND TELECOMMUNICATION

NUMBER: 264/DIRJEN/2005

ON

TECHNICAL REQUIREMENTS OF TOOLS AND EQUIPMENT OF

CUSTOMER PREMISES EQUIPMENT (CPE) UNIVERSAL MOBILE TELECOMMUNICATION SYSTEM – TIME DIVISION DUPLEXING

(UMTS – TDD)

BY THE GRACE OF GOD THE ALMIGHTY

DIRECTOR GENERAL OF POST AND TELECOMMUNICATION

Considering:          a.  that   the   Decision   of   the   Minister of   Communication

Number:   KM 3  Year 2001 on Technical Requirements of

Telecommunication  Tools  and   Equipment stipulates that

every telecommunication tool and equipment shall fulfil the

technical requirements;

- that in order to implement the provision of Article 3 of the  Decree of the Minister of Communication Number: KM.10 Year 2005 on Certification of Telecommunication Tools and Equipment, any testing of telecommunication tools and equipment must be based on technical requirements as determined by the Director General;

- that in view of what is stated in points a and b above, it is considered necessary to ratify a Decree of the Director General of Post and Telecommunication on Technical Requirements   of   Tools and Equipment of Customer Premises Equipment (CPE) Universal Mobile Telecommunication System – Time Division Duplexing (UMTS – TDD)

Bearing in mind: 1.  Law of the Republic of Indonesia Number 36 Year 1999 on

Telecommunication   (State  Gazette  of  the  Republic   of

Indonesia   Number   154   Year  1999,   Additional    State

Gazette of the Republic of Indonesia Number 3881);

- Government Regulation of the Republic of Indonesia Number 52 Year 2000 on Provision of Telecommunication (State Gazette of the Republic of Indonesia Number 107 Year 2000, Additional State Gazette of the Republic of Indonesia Number 3980);

- Government Regulation of the Republic of Indonesia Number 53 Year 2000 on Use of Radio Frequency Spectrum and Satellite Orbit (State Gazette of the Republic of Indonesia Number 108 Year 2000, Additional State Gazette of the Republic of Indonesia Number 3981);

- Decree of the President of the Republic of Indonesia Number 9 Year 2005 on Positions, Tasks, Functions, Organizational Structure and Working of State Ministries  of the Republic of Indonesia;

- Decree of the President of the Republic of Indonesia Number 10 Year 2005 on Organizational Units and Functions of Echelon I of State Ministries of the Republic of Indonesia as amended by the Decree of the President of the Republic of Indonesia Number 15 Year 2005;

- Decision of the Minister of Communication Number KM.3 Year 2001 on Technical Requirements of Telecommunication Tools and Equipment;

- Decree of the Minister of Communication Number KM.10 Year 2005 on Certification of Telecommunication Tools and Equipment;

- Decree of the Minister of Communication and Information Technology Number 01/P/M.Kominfo/1/2005 on Organizational Structure and Working of the Department of Communication and Information Technology.

DECIDES

To ratify            :	DECREE OF THE   DIRECTOR   GENERAL  OF  POST AND

TELECOMMUNICATION ON TECHNICAL  REQUIREMENTS                      OF TOOLS AND EQUIPMENT OF CUSTOMER PREMISES EQUIPMENT (CPE) UNIVERSAL MOBILE TELECOMMUNICATION SYSTEM – TIME DIVISION DUPLEXING (UMTS – TDD)

Article 1

The Tools and Equipment of Customer Premises Equipment (CPE) Universal Mobile Telecommunication System – Time Division Duplexing (UMTS – TDD) shall follow the technical requirements as stipulated in the Attachment of this Decree.

Article 2

The implementation of certification of Tools and Equipment of Customer Premises Equipment (CPE) Universal Mobile Telecommunication System – Time Division Duplexing (UMTS – TDD) shall be guided by the technical requirements as stipulated in Article 1.

Article 3

This Decree shall come into force as from the date of its ratification.

Done at:             JAKARTA

On       :  October 12, 2005

_____________________

DIRECTOR GENERAL OF POST AND TELECOMMUNICATION

Signed

BASUKI YUSUF ISKANDAR

Copies of this Decree are sent to:

- Minister of Communication and Information Technology;

- Secretary of the Directorate General of Post and Telecommunication;

- Directors within the Directorate General of Post and Telecommunication;

- Head of the House of Telecommunication Equipment Testing.

ATTACHMENT:  DECREE OF THE DIRECTOR GENERAL

OF POST AND TELECOMMUNICATION

NUMBER          :  264/DIRJEN/2005

DATE                :  October 12, 2005

________________________________________________

TECHNICAL REQUIREMENTS OF TOOLS  AND EQUIPMENT OF CUSTOMER PREMISES EQUIPMENT (CPE) UNIVERSAL MOBILE TELECOMMUNICATION SYSTEM – TIME DIVISION DUPLEXING (UMTS – TDD)

CHAPTER I

GENERAL PROVISIONS

A.	Scope

These technical requirements cover: scope, definitions, abbreviations, application, general characteristics, main characteristics, and their testing requirements.

- Definition

- CPE UMTS-TDD is an instrument installed and placed at the customer premises and generally called MODEM (Modulator/DEModulator) UMTS-TDD, where that modem may take the form of Desktop and also PCMCIA.

- MODEM is an electronic equipment that functions for changing signal into data. UMTS-TDD Modem transmits data via air (air-interface).

C.	Abbreviations

CISPR	: The International Special Committee on Radio Interference

CPE	: Customer Premises Equipment

Mcps	: Mega chip per second

Modem	: Modulator Demodulator

PCMCIA	: Personal Computer Memory Card International Association

TDD	: Time Division Duplexing

UE	: User Equipment

UMTS	: Universal Mobile Telecommunication System

CHAPTER II

TECHNICAL CHARACTERISTICS

- General Characteristics

  - Modem is meant only to be used for communication within the building or operates in localized area.

  - Modem is meant to operate together in a frequency range and in its operation it will not cause interference towards other radio communication equipment.

B.	Main Characteristics

  - Frequency Ranges

Frequency that can be used at UMTS-TDD Modem is 2053 -2082 MHz.

Allocation and frequency are determined by the Directorate of Radio Frequency Spectrum and Satellite Orbit.

- Transmitter Antenna

Transmitter Antenna must be integrated with its equipment

- Receiver Sensitivity

Maximum receiver sensitivity must not be more than -113 dBm at 3.84 Mcps and -110 dBm at 7.68 Mcps.

- Transmit Power

Transmit Power must not be more than 24 dBm +1/-3 dB.

- Radiated Emission Limits

Refer to CISPR 22 and 24 or equivalent standard

- Display Indicator

Possessing indicator to show condition of power and connectivity.

CHAPTER III

TESTING REQUIREMENTS

  - Method of Selecting Testing Sample

Selection of testing materials is carried out by random sampling according to the prevailing testing procedure.

B.	Testing Method

The testing method is defined by the testing institution which is capable of showing in a qualitative and quantitative manner that the testing materials comply with the technical requirements.

C.	Conditions for Passing the Test

The testing result is declared PASS THE TEST, if all the testing materials comply with the provisions contained in the technical requirements.

If the testing materials are declared  DO NOT PASS THE TEST, all the groups belonging to the testing materials are also declared not passing the test.

D.	Conditions of Safety and Health

The relevant Tools and Equipment must be engineered in such a way that users are protected from electrical and electromagnetic disturbances.

- Conditions of Labelling

Every relevant Tool and Equipment shall be labelled, containing the name of the manufacturer and manufacturing country, brand, type, and serial number and must fulfil the conditions of certification.

Done at:              JAKARTA

On        :  October 12, 2005

______________________

DIRECTOR GENERAL OF POST AND TELECOMMUNICATION,

Signed

BASUKI YUSUF ISKANDAR