DECREE OF THE DIRECTOR GENERAL OF POST AND TELECOMMUNICATION

NUMBER: 266/DIRJEN/2005

ON

TECHNICAL REQUIREMENTS OF MARITIME RADIO TOOLS AND EQUIPMENT

BY THE GRACE OF GOD THE ALMIGHTY

DIRECTOR GENERAL OF POST AND TELECOMMUNICATION

Considering:          a.  that   the   Decision   of   the   Minister of   Communication

Number:   KM 3  Year 2001 on Technical Requirements of

Telecommunication  Tools  and   Equipment stipulates that

every telecommunication tool and equipment shall fulfil the

technical requirements;

- that in order to implement the provision of Article 3 of the  Decree of the Minister of Communication Number: KM.10 Year 2005 on Certification of Telecommunication Tools and Equipment, any testing of telecommunication tools and equipment must be based on technical requirements as determined by the Director General;

- that in view of what is stated in points a and b above, it is considered necessary to ratify a Decree of the Director General of Post and Telecommunication on Technical Requirements   of   Maritime  Radio Tools and  Equipment.

Bearing in mind: 1.  Law of the Republic of Indonesia Number 36 Year 1999 on

Telecommunication   (State  Gazette  of  the  Republic   of

Indonesia   Number   154   Year  1999,   Additional    State

Gazette of the Republic of Indonesia Number 3881);

- Government Regulation of the Republic of Indonesia Number 52 Year 2000 on Provision of Telecommunication (State Gazette of the Republic of Indonesia Number 107 Year 2000, Additional State Gazette of the Republic of Indonesia Number 3980);

- Government Regulation of the Republic of Indonesia Number 53 Year 2000 on Use of Radio Frequency Spectrum and Satellite Orbit (State Gazette of the Republic of Indonesia Number 108 Year 2000, Additional State Gazette of the Republic of Indonesia Number 3981);

- Decree of the President of the Republic of Indonesia Number 9 Year 2005 on Positions, Tasks, Functions, Organizational Structure and Working of State Ministries  of the Republic of Indonesia;

- Decree of the President of the Republic of Indonesia Number 10 Year 2005 on Organizational Units and Functions of Echelon I of State Ministries of the Republic of Indonesia as amended by the Decree of the President of the Republic of Indonesia Number 15 Year 2005;

- Decision of the Minister of Communication Number KM.3 Year 2001 on Technical Requirements of Telecommunication Tools and Equipment;

- Decree of the Minister of Communication Number KM.10 Year 2005 on Certification of Telecommunication Tools and Equipment;

- Decree of the Minister of Communication and Information Technology Number 01/P/M.Kominfo/1/2005 on Organizational Structure and Working of the Department of Communication and Information Technology.

DECIDES

To ratify            :	DECREE OF THE   DIRECTOR   GENERAL  OF  POST AND

TELECOMMUNICATION ON TECHNICAL  REQUIREMENTS                      OF    MARITIME    RADIO    TOOLS    AND       EQUIPMENT

Article 1

The Maritime Radio Tools and Equipment shall fulfil the technical requirements as indicated in the Attachment of this Decree.

Article 2

The implementation of certification of Maritime Radio Tools and Equipment shall be guided by the technical requirements as stipulated in Article 1.

Article 3

This Decree shall come into force as from the date of its ratification.

Done at:             JAKARTA

On       :  October 12, 2005

_____________________

DIRECTOR GENERAL OF POST AND TELECOMMUNICATION

Signed

BASUKI YUSUF ISKANDAR

Copies of this Decree are sent to:

- Minister of Communication and Information Technology;

- Secretary of the Directorate General of Post and Telecommunication;

- Directors within the Directorate General of Post and Telecommunication;

- Head of the House of Telecommunication Equipment Testing.

ATTACHMENT :  DECREE OF THE DIRECTOR GENERAL

OF POST AND TELECOMMUNICATION

NUMBER          :  266/DIRJEN/2005

DATE                :  October 12, 2005

________________________________________________

TECHNICAL REQUIREMENTS OF MARITIME RADIO

TOOLS  AND EQUIPMENT

CHAPTER I

GENERAL PROVISIONS

A.	Scope

These technical requirements cover: scope, definitions, abbreviations, technical characteristics and testing requirements of tools and equipment of Non GMDSS (Global Maritime Distress and Safety System) radio and  equipment of GMDSS radio.

The Maritime Radio Equipment must comply with international provisions namely International Maritime Organization (IMO), International Telecommunication Union (ITU), International Electrotechnical Commission (IEC), Safety Of Life At Sea (SOLAS), European Committee on Post and Telecommunication (CEPT), and Federal Communications Commission (FCC).

B.	Definition

Maritime Radio Equipment of Non GMDSS is a communication equipment that works at maritime frequency band and functions as telephony radio telecommunication.

The Maritime Radio Equipment of GMDSS is a radio equipment that fulfils the provision of global communication system in the maritime world applicable throughout the world either using (radio) terrestrial network or satellite, enabling ships in a distress situation (accident, sinking, etc.)  send distress messages in the form of telephony or digital selective calling (DSC) through various automatic radio communication systems to all ships and Base/Coastal Stations situated near the place of occurrence or to  a maritime authority.

C.	Abbreviations

- dBc              : Decibel Coefficient

- dB                : Decibel

- DC              : Direct Current

- DSC            : Digital Selective Calling

- EPIRB         : Emergency Position Indicating Radio Beacon

- GHz             : Giga Hertz

- GMDSS       : Global Maritime Distress and Safety System

- GPS             : Global Positioning System

- HF                : High Frequency

- Hz                : Hertz

- KHz              : Kilo Hertz

- MF                : Medium Frequency

- MHz              : Mega Hertz

- Navtex          : Navigational Telex

- ppm              : part per million

- RF                : Radio Frequency

- SART           : Search and Rescue Transponder

- SHF             : Super High Frequency

- UHF             : Ultra High Frequency

- USB             : Universal Serial Bus

- VDC             : Voltage Direct Current

- VHF             : Very High Frequency

- Wpep           : Watt peak emission power

- W                 : Watt

- µV                : micro Voltage

CHAPTER II

TECHNICAL CHARACTERISTICS

For radio transmitter equipment of HF, VHF, UHF, their frequency must be determined by special equipment (Programming by Vendor/Manufacturer, not by users) in line with the frequency determined in the license.

- Maritime Radio Equipment of Non GMDSS

  - VHF Radio Transmitter

    - Work frequency of Marine Band

-	Ship Station                                	: 149.30 – 163.75 MHz

-	Base/Coastal Station 	   : 149.30 – 163.75 MHz

-	Handy Talky/Portable Radio            : 155 -163 MHz

    - Spurious Emission                                 : 0.1 µW (-70dB)

    - Frequency Stability                                : ± 10 ppm, opt 5 ppm

    - RF Carrier spacing                               : 12.5 KHz and 25 KHz

    - Modulation system                                 : FM

    - Modulation Deviation                              : ± 5 KHz

    - Audio Distortion (ref. 1000 Hz)              : < 5%

    - Transmitter Power Class

-	Ship Station                                    : 25 Watt ± 10%

-	Base/Coastal Station                      : 25 – 50 Watt ± 10%

-	Handy Talky/Portable Radio           : 1 – 5 Watt ± 10%

    - Difference in spacing of Dupplex Tx/Rx: 4.5 MHz

    - Modulation Class                                  : G3EJN (F3B) or

16KOG3E (G3E)

    - MF/HF Radio Transmitters

      - Work Frequency of Marine Band                 : 1.6 MHz – 30 MHz

      - Spurious Emission                                       : - 60 dB/PEP (peak

emission power)

      - Frequency Stability                                      : 0.35 ppm

      - RF Carrier resolution                                   : 100 Hz

      - Modulation system                                      :  AM, USB

      - Modulation Deviation                                  :  30%

      - Audio Distortion (ref. 1 KHz/USB/14mv)     : < 0.5%

      - Transmitter Power Class

-	Base Station                                          : 250 W, 500 W, 1000 W

-	Ship Station                                           : 100 W, 150 W, 250 W,

500 W

      - Modulation Class                                        : Telephony mode J3E

or H3E

- Maritime Radio Equipment of GMDSS

- VHF Radio Transmitter

  - Work Frequency of Marine Band

-	Ship Station                                        : 149.30 – 163.75 MHz

-	Base/Coastal Station                          : 149.30 – 163.75 MHz

-	Handy Talky/Portable Radio               : 155 – 163 MHz

    - Distress Frequency (Ch 70 DSC)             : 156.525 MHz

    - Spurious Emission                                    : 0.1 µW (-70dB)

    - Frequency Stability                                   : ± 10 ppm, opt 5 ppm

    - RF Carrier spacing                                    : 12.5 KHz and 25 KHz

    - Modulation system                                    :  FM

    - Modulation Deviation                                : ±  5 KHz

    - Audio Distortion (ref. 1000Hz)                   : < 5%

    - Transmitter Power Class

-	Ship Station                                         : 25 Watt ± 10%

-	Base/Coastal Station                           : 25 - 50 Watt ± 10%

-	Handy Talky/Portable Radio                : 1 – 5 Watt ±  10%

    - Difference in spacing of Dupplex Tx/Rx    : 4.5 MHz

    - Modulation Class                                       : G3EJN (F3B) or 16KOG3E

(G3E)

DSC G2B or 16KOG2B

- MF/HF Radio Transmitters

- Work frequency of Marine band                : 1.6 MHz – 30 MHz

- Distress Frequency (DSC)                        :  2187.5 KHz, opt. 4207.5

KHz, 6312 KHz, 8414.5

KHz, 12577 KHz, 16804.5

KHz.

- Spurious Emission                                    : - 60 dB/PEP (peak emission

power)

- Frequency Stability                                   : 0.35 ppm

- RF Carrier resolution                                 :  100 Hz

- Modulation system                                    :  AM, USB

- Modulation Deviation                                 :  30%

- Audio Distortion (ref.1KHz/USB/14mv)     :  < 0.5%

- Transmitter Power Class

-	Base Station                                        : 250 W, 500 W, 1000 W

-	Ship Station                                         : 100 W, 150 W, 250 W,

500 W.

J	Modulation Class                                      : Telephony mode USB (J3E)

or HEJ DSC mode CW

(AIA)

- Radar Transponder Equipment of SART 9 GHZ

- Receiver Response       : 9.2 – 9.5 GHz, sensitive better than – 50dBm

- Transmitter Response   : 12 forward and return sweeps through the

range 9.2 – 9.5 GHz  nominal sweeps times

7.5 µs forward and 0.4 µs return.

Minimum recovery time following excitation,

less than 10 µs. Response reply to receiver

signal less than 0.5 µs.

- Radiated Power (ERP)  : > 400 mW e.i.r.p (+ 26 dBm)

- Duration of operation     : 96 hours in standby condition followed by a

minimum 8 hours of transmission while being

continually interrogated with a pulse

repetition frequency of  1 KHz.

  - Temperature Range      : -20oC to +55oC operational

-30oC to +65oC storage

  - Antenna characteristics : Vertical beamwidth at least +/- 12.5

degrees relative to the horizontal plane of the

radar transponder .

Azimuthal beamwidth omnidirectional  to +/-

2dB.

  - Effective Antenna Height: 1 meter or greater.

- Equipment of Emergency Position Indicating Radio Beacon (EPIRB)

  - General

Message Format         : Serialised, Maritime Mobile Service Identity

(MMSI) and radio call sign.

Programming              :  Via RS232 light pen and Windows based PC.

Temperature               :  Operating -40oC to +55oC (Class 1)

Storage -40oC to +70oC

Battery Life                  :  5 years storage then 48 hours operation

Sealing depth              :  Waterproof to 10 m.

- Transmitter T406 MHZ

Frequency                   : 406.025 MHz ± 2kHz

Output Power              : 5W ± 2dB

Modulation                  : Biphase 1.1 ± 0.1 radiance

- Transmitter 121.5 MHz

Frequency                   : 121.5 MHz  ± 3kHz

Output Power              : 50mW ERP

Modulation                  : AM, up or down swept tone

- Visual Location

Intensity                      : 0.75Cd Xenon discharge light

Flash Rate                  :  23 flashes per minute

- Navtex Equipment

  - Receiving frequency            : 518 kHz

  - Receiving mode                   : F1B NAVTEX broadcast

  - Message Format                  : according to CCIR 625-1, collective B mode

  - Call Sensitivity                     : < -6 dBuV at 50 ohm active antenna

< 4 uF at 10 ohm/150 pF antenna

    - Intermodulation                      : Unwanted signal of > 70 dBuV will not

an error rate > 4% at 20 dBuV input level.

    - Spurious Emission               : < 1 nF

    - Antenna Input Impedance    : 50 ohm or 10 ohm / 150 pF selectable.

    - Active Antenna                     : 1.5 m whip with integrated preAmp,

508 to 528 kHz with 30 m coaxial cable

    - Input protection                   : 30 Vms for 15 min

    - Printer

- Recording Type                : 5x7 dot matrix thermal head printer,

42 characters/line

- Print Speed                         : approx. 70 cps

- Paper Roll                         : 112 mm broad, 30 m long

          - Controls

- Dimmer                             : 3 steps

- Message Selection           : All types except  A, B, D, L direct printing of

A, B, D  & L messages only when

corresponding stations are selected.

- NAVTEX Stations               : All Stations from A to Z

Selection

- Receiver Selection             : Internal or external (if connected)

- Built-inTest                       : Memory, receiver part, printer, display, alarm

- Inmarsat-C Equipment

- Maritime Aerial                   : Inmarsat C/GPS omnidirectional aerial,

RHC polarized G/T – 23 dB/K, EIRP 14 dBW

at 5o  elevation. Coverage +90o  to -15o .

- Transmit Frequencies        : 1626.5 – 1660.5 MHz

- Receive Frequencies         : Inmarsat C 1525.0 MHz to 1559.0 MHz .

GPS 1575.42 MHz.

  - Channel Spacing               : 1.25/2.5/5 MHz

  - Modulation                         : 1200 symbols/sec. BPSK

  - Data Rate                          : 600 bit/sec.

  - Aerial Interface                  : Standard 50 ohm female TNC (transceiver),

female TNC (aerial)

  - Printer Interface                 : Standard parallel Centonics, DB-25F

connector.

  - Parallel I/O                         : RS-410 4-bit open collector input/output and

2-bit input.

  - Arc Net Interface                : ATA/ANSI 878.1 2.5Mbit token based, twisted

pair.

  - GPS module                       : 8-channel GPS tamper proof PC-board, 1 sec.

update rate, 15 m RMS accuracy (100 m with

S/A), 0.2 m RMS velocity accuracy.

  - Sleep Mode                         : Timer and event programmable modes; total

system power consumption with the following

reporting intervals 1.14W/ 15 min, 570

mW/30min, 280mW / 1 h, 140 mW/ 2 h, 60

mW/5 h, 30 mW/10 h.

  - Solid State Storage            : 512 kbyte Flash and 256 kbyte SRAM.

  - DC Power Source              : 10-32 V floating DC4.8/81 W RX/TX (with GPS

module)

  - Ambient Temperature        : Electronics Unit, -25o C to 55o C operating,

- 40o C to 80o C storage.

  - Solar Radiation                  : 1200W/m2 max. flux density

  - Relative Humidity               : 95% non-condensing at 40oC

  - Ice                                      : Up to 25 mm (EME)

Up to 10 cm/hour, droplet size.

  - Precipitation                       : 0.5-4.5 mm (EME)

  - Wind                                   : Up to 200 km/hour

  - Vibration Operational          : Random 5-20 Hz 0.005g2/Hz

20-150 Hz – 3 dB/ct.0 (0.5g nms)

CHAPTER III

TESTING REQUIREMENTS

  - Method of Selecting Testing Sample

Selection of testing materials is carried out by random sampling according to the prevailing testing procedure.

B.	Testing Method

The testing method is defined by the testing institution which is capable of showing in a qualitative and quantitative manner that the testing materials comply with the technical requirements.

C.	Conditions for Passing the Test

The testing result is declared PASS THE TEST, if all the testing materials comply with the provisions contained in the technical requirements.

If the testing materials are declared  DO NOT PASS THE TEST, all the groups belonging to the testing materials are also declared not passing the test.

D.	Conditions of Safety and Health

The relevant Tools and Equipment must be engineered in such a way that users are protected from electrical and electromagnetic disturbances.

- Conditions of Labelling

Every relevant Tool and Equipment shall be labelled, containing the name of the manufacturer and manufacturing country, brand, type, and serial number and must fulfil the conditions of certification.

Done at:              JAKARTA

On        :  October 12, 2005

______________________

DIRECTOR GENERAL OF POST AND TELECOMMUNICATION,

Signed

BASUKI YUSUF ISKANDAR