DECREE OF THE DIRECTOR GENERAL OF POST AND TELECOMMUNICATION

NUMBER : 96/DIRJEN/2008

ON

TECHNICAL REQUIREMENTS OF TELECOMMUNICATION ANTENNA TOOLS AND EQUIPMENT OF BROADBAND WIRELESS ACCESS (BWA) NOMADIC AT FREQUENCY BAND OF 2.3 GHz

BY THE GRACE OF GOD THE ALMIGHTY

DIRECTOR GENERAL OF POST AND TELECOMMUNICATION

Considering:          a. that the Decision of the Minister of Communication Number

KM. 3 Year 2001 on Technical Requirements of

Telecommunication Tools and Equipment stipulates that

every telecommunication tool and equipment shall fulfil the

technical requirements;

b. that pursuant to the provision of Article 3 of the Decree  of

the Minister of Communication Number KM. 10 Year 2005

on Certification of Telecommunication Tools and

Equipment, any testing of telecommunication tools and

equipment shall be based on technical requirements as

determined by the Director General;

c. that based on considerations mentioned in points a and b

above, it is considered necessary to ratify the Decree of the

Director General of Post and Telecommunication on

Technical Requirements of Telecommunication Antenna

Tools and Equipment of Broadband Wireless Access (BWA)

Nomadic at Frequency Band of 2.3 GHz.

Bearing in mind:   1.  Law of the Republic of Indonesia Number 36 Year 1999 on

Telecommunication (State Gazette Number 154 Year 1999,

Additional State Gazette Number 3881);

.

- Government Regulation of the Republic of Indonesia Number 52 Year 2000 on the Provision of Telecommunication (State Gazette Number 107 Year 2000, Additional State Gazette Number 3980);

- Government Regulation of the Republic of Indonesia Number 53 Year 2000 on the Use of Radio Frequency Spectrum and Satellite Orbit (State Gazette Number 108 Year 2000, Additional State Gazettte Number 3981);

- Decree of the President of the Republic of Indonesia Number 9 Year 2005 on Positions, Tasks, Functions Organizational Structure and Working of State Ministries of the Republic of Indonesia;

- Decree of the President of the Republic of Indonesia Number 10 Year 2005 on Organizational Units and Functions of Echelon I of State Ministries of the Republic of Indonesia as amended by  the Decree of the President of the Republic of Indonesia Number 7 Year 2007;

- Decision of the Minister of Communication Number 3 Year 2001 on Technical Requirements of Telecommunication Tools and Equipment;

- Decree of the Minister of Communication Number KM.10 Year 2005 on Certification of Telecommunication Tools and Equipment;

- Decree of the Minister of Communication and Information Technology Number 01/P/M.Kominfo/1/2005 on Organizational Structure and Working of the Department of Communication and Information Technology;

- Decree of the Minister of Communication and Information Technology Number 03/P./M./Kominfo/5/2005 Year 2005 on Adjustment of Nomenclatures of a number of Decisions/Decrees of the Minister of Communication which regulate Special Material Contents in the field of Post and Telecommunication.

DECIDES

To ratify    DECREE OF THE DIRECTOR GENERAL OF POST AND TELECOMMUNICATION ON TECHNICAL REQUIREMENTS OF TELECOMMUNICATION ANTENNA TOOLS AND EQUIPMENT OF BROADBAND WIRELESS ACCESS (BWA) NOMADIC AT FREQUENCY BAND OF 2.3 GHz

Article 1

The Telecommunication Antenna Tools and Equipment of Broadband Wireless Access (BWA) Nomadic at Frequency Band of 2.3 GHz shall fulfil the technical requirements as stated in the Attachment of this Decree.

Article 2

The implementation of certification of telecommunication Antenna Tools and Equipment of Broadband Wireless Access (BWA) Nomadic at Frequency Band of 2.3 GHz shall fulfil the technical requirements as stipulated in Article 1.

Article 3

This Decree is coming into force as from the date of its ratification.

Done at:              JAKARTA

On        : February 26, 2008

_____________________

DIRECTOR GENERAL OF POST AND TELECOMMUNICATION

Signed

BASUKI YUSUF ISKANDAR

Copies of this Decree are sent to:

- Minister of Communication and Information Technology;

- Secretary of the Directorate General of Post and Telecommunication;

- Directors within the Directorate General of Post and Telecommunication;

- Head of Testing Institute of Telecommunication Equipment

ATTACHMENT: DECREE OF THE DIRECTOR GENERAL

OF POST AND TELECOMMUNICATION

NUMBER         : 96/DIRJEN/2008

DATE               : FEBRUARY 26, 2008_________________

CHAPTER I

GENERAL PROVISIONS

- Scope

These technical requirements cover the scope, definition, acronyms, system characteristics, telecommunication Antenna tools and equipment of Broadband Wireless Access Nomadic at frequency band of 2.3 GHz, hereinafter called     BWA 23 Antenna.

- Definition

What is meant by tools and equipment BWA 23 Antenna in this standard is a part of  BWA 23 radio communication system which forms the interface between radio system and external environment that works at frequency band of 2,300 – 2,390 MHz.

- Acronyms

- BS            : Base Station

- BWA        : Broadband Wireless Access

- CPE         : Customer Premises Equipment

- dB            : Decibell

- dBi           : Decibell Isotropic

- dBm         : Decibell Milliwatt

- DC           : Direct Current

- EIRP        : Effective Isotropically Radiated Power

- Mbps       : Mega byte per second

- MHz         : Mega Hertz

- N              : A kind of connector

- PMP         : Point-to-Multi Point

- PTP          : Point-to-Point

- RF            : Radio Frequency

- SMA         : A kind of connector

- SS            : Subscriber Station

- TDD          : Time Division Duplex

- VSWR       : Voltage Standing Wave Ratio

- XPD          : Cross Polarization Discrimination

- Terms

For the purpose of this standardization, some terms are defined as follows:

- Base Station               : A set of equipment having the functions of

providing connectivity, management and control

on SS.

- Broadband                 : The capability to transfer data more than 1.5 Mbps

and or to use total bandwidth of  minimum 1 MHz.

- Broadband                  : Broadband wireless access network

Wireless Access

- Output Power              : Power put out of transmitter equipment

- CPE                             : Network termination equipment  of customer

side.

- dBi                               : Gain of one antenna against isotropic antenna as

a reference

- EIRP                            : Measured power level transmitted by antenna.

- BWA Network              : A collection of elements of broadband wireless

access network comprising BS and SS.

  - Nomadic                      : Application of wireless access where location of

terminal end user may be shifted and when in use,

the terminal end user may not move.

  - Subscriber Station       : BWA equipment located at the customer side.

  - Telecommunication     : Any transmission, emission or reception of any

kind of sign, image, sound and information in any

form by wire, optic, radio or other electromagnetic

systems.

- XPD                             : Comparison between maximum co-polar radiation

and minimum cross-polar radiation.

- Reference Model

6.	Entity Model

Below is the explanation of entities found in reference model

6.1	BS

- Is an equipment having the function of data transmission centre.

- Has a function as coordination centre for management of resources (radio)

6.2	SS

- Is a network termination equipment on the part of the customer (CPE).

- Has a function as customer’s data transmission means.

6.3	BS Antenna and SS Antenna

- Are the transmission equipment having the function  of altering electrical energy  into electromagnetic radio wave.

7.	Reference Point

7.1	U

- BWA Radio Interface

7.2	U’

- Reference point between BS or SS and Antenna.

CHAPTER II

GENERAL AND OPERATIONAL CHARACTERISTICS

- The BWA 23 Antenna system has the capability to enable the provision of reliable broadband wireless communication, both for urban, sub-urban and rural areas.

- The BWA 23 Antenna is classified based on radiation pattern into:

- omni

- directional

- sectoral

  - The BWA 23 Antenna is classified based on application into:

- Point-to-point (PTP)

  - Point-to-Multipoint (PMP)

4.	The BWA 23 Antenna is classified based on the kinds of BWA 23 equipment:

- BS Antenna

- SS Antenna

CHAPTER III

TECHNICAL REQUIREMENTS OF TELECOMMUNICATION TOOLS AND  EQUIPMENT

1.	Base Station

| Electrical Parameter | Value |
| --- | --- |
| Frequency Range | 2,300 – 2,390 MHz |
| Gain | Sectoral : Minimum 15 dBi Omni : Minimum 9 dBi |
| Impedance | 50 Ώ |
| Polarization | Vertical |
| VSWR | Maximum 1.9 : 1 |
| Maximum Power Input | 50 W |
| XPD | Minimum 20 dB |
| Connector | N Female |

| Environmental Parameter | Value |
| --- | --- |
| Resistant capacity against wind speed | Maximum 200 km/hour |
| Front wind load | 110 Newton |
| Lateral wind load | 75 Newton |
| Grounding/Lightning Protection | DC grounded |
| Temperature | Maximum 65ºC |
| Humidity | 100% |

2.	Subscriber Station

| Electrical Parameter | Value |
| --- | --- |
| Frequency Range | 2,300 – 2,390 MHz |
| Gain | Maximum 15 dBi |
| Impedance | 50 Ώ |
| Polarization | Vertical |
| VSWR | Maximum 1.9 : 1 |
| Maximum Power Input | 50 W |
| XPD | Minimum 20 dB |
| Connector | N-Female or SMA-female |

| Environmental Parameter | Value |
| --- | --- |
| Resistant capacity against wind speed | Outdoor : maximum 100 km/hour |
| Front wind load | Outdoor : maximum 55 Newton |
| Grounding/Lightning Protection | DC grounded |
| Humidity | Outdoor : maximum 100% Indoor : maximum 95% |
| Temperature | Outdoor : maximum 65ºC Indoor : maximum 40ºC |

3.	Documentation

The equipment is furnished with technical documentation concerning the guide for use and the relevant specification in Indonesian language.

CHAPTER IV

TESTING REQUIREMENT

1	The Sampling Method

The sampling of the equipment to be tested is carried out in accordance with the testing  procedure with the minimum number of two units.

2	The Testing Method

The testing method of the equipment is stipulated in a separate document. The testing method must be capable of showing in a qualitative and quantitative manner that the tested equipment fulfils the requirement of this standard.

3	The Safety and Health  Requirement

This BWA 23 Antenna Equipment must undergo a consruction design in such a way that the user is protected from electric and electromagnetic disturbances.

4	The Electromagnetic Compatibility Requirement

This is to be referred to CISPR-22 and CISPR-24 Standards

5	The Marking Requirement

Every BWA 23 Antenna Equipment shall be marked with the names of the factory and the producing country, the brand/type and serial number.

Done at:              JAKARTA

On        : February 26, 2008

_____________________

DIRECTOR GENERAL OF POST AND TELECOMMUNICATION

Signed

BASUKI YUSUF ISKANDAR

# Text boxes

Antena

SS

Standardization  Coverage

BS

U’

BS

Antenna

U’

SS

Antenna

U

Station

Subscriber

Base Station